## Slide 1
THEREMINO SYSTEM
cycle of workshop
Day 1:
  Basic function
  Programming
Leonardo De Palo Ph.D. leo.depalo@theremino.com www.theremino.org
L1-Buildingg A2, Hangcheng Innovation Park, Xixiang Street, Bao’an Districh, Shenzhen, China

## Slide 2: Day -1-
Colorful igloo
Basic functions of THEREMINO SYSTEM.
  The SLOT
  The HAL
  Sensors
  Actuators
  HAL integrated scope
  SlotVieWer
  Slot naming
Programming
  The AUTOMATION LANGUAGE
    Variable assignment
    Buttons – text, slot, color, labels, enable/disable
    For- next, with step, instead of while
    Goto - Gosub - Return
    If - Else – Endif
    Select case

## Slide 3: 插槽 The SLOT
The concept of slots is easily understood by looking at the mailbox slots.
Or the airport slots where the airline manages its slot as it wishes, lines, charter, cargo or resell it.
Or like the trolleys in a mine that can hold different materials.
通过查看邮箱插槽，可以轻松理解插槽的概念。
或者航空公司按照自己的意愿管理其航班时刻、航线、包机、货运或转售的机场航班时刻。
或者像矿井中的手推车一样可以容纳不同的材料。

## Slide 4: 插槽 The SLOT
The MAIL SLOT is the place where letters, invoices, newspapers, advertisements, etc. are put
A slot can hold different things at different times.
One application writes in a slot and another application reads the slot and makes decisions based on the value it finds.
MAIL SLOT 是放置信件、发票、报纸、广告等的地方
一个插槽可以在不同的时间容纳不同的东西。
一个应用程序写入一个插槽，另一个应用程序读取该插槽并根据它找到的值做出决定。

## Slide 5: 插槽 The SLOT
在 Theremino 系统中, 单词 "slot" 标识一个简单的容器来传输数据。
有2000个插槽。 1000 个时隙发送数据。 1000 个插槽来读取数据。
这些插槽位于个人计算机内存的一部分中，也可以从其他应用程序访问。 每个插槽都有自己的特定标识号和可选的唯一名称。
插槽用于高速发送和接收数据
到 Theremino 大师。
操作插槽只有两个简单的指令：
读槽：variable = Slot (nn)
写槽： Slot (nn) = variable
In the Theremino system, the word "slot" identifies a simple container to transfer data.
There are 2000 slots. 1000 slots to send data. 1000 slots to read data.
The slots reside in a part of the Personal Computer's memory that is also accessible from other applications. Each slot has its own specific identification number and optionally a unique name.
The slots are used to send and receive data at high speed
to Theremino Master.
There are only two simple instructions to manipulate the slots:
reading slot: variable = Slot (nn)
write slot: Slot (nn) = variable
5
https://www.theremino.com/en/technical/communications#slot
English
中国人
https://www.theremino.com/zh/technical/communications#slot

## Slide 6: 哈尔 The HAL
The HAL (Hardware Abstraction Layer) module takes care of the interfacing and signal processing functions present in the slots.
Allows you to assign to each of the 12 I / O pins the internal functions of the PIC microprocessor present in the PCBA Theremino Master.
Allows communication with PC via USB in HID mode.
It typically transfers over 700 slots bi-directionally.
HAL（硬件抽象层）模块负责插槽中的接口和信号处理功能。
允许您将 PCBA Theremino 主控器中存在的 PIC 微处理器的内部功能分配给 12 I / O 引脚中的每一个。
允许在 HID 模式下通过 USB 与 PC 通信。
它通常双向传输 700 多个插槽。
https://https://www.theremino.com/en/downloads/foundations#hal
https://https://www.theremino.com/zh/downloads/foundations#hal
English
中国人

## Slide 7
  传感器和执行器 Sensors and actuators
由于 Arduino 开源系统，带有 Master 的 theremino 系统管理市场上几乎所有的传感器和执行器。
The theremino system with its Master manages almost all sensors and actuators on the market thanks to Arduino open source systems.

## Slide 8
  传感器和执行器 Sensors and actuators
您可以花很少的钱找到在线传感器和执行器套件，其中包含：
Tor little money you can find online sensor and actuator kits that contain:
Kit Includes:
1 x Mercury sensor + LED module KY-027
1 x Rotary encoder module KY-040
1 x Optocoupler module KY-010
1 x Pulse sensor KY-039
1 x Reed relay module KY-025
1 x Obstale sensor module KY-032
1 x Line following sensor module KY-033
1 x Microphone module KY-038
1 x Laser module KY-008
1 x 5V relay module KY-019
1 x Temperature module module (DS18B20) KY-001
1 x Temperature module module (LM35) KY-028
1 x Linear magnetic sensor module KY-024
1 x Fire sensor module KY-026
1 x Sensitive microphone module KY-037
1 xTemperature and humidity sensor module (DHT11) KY-015
1 x XY joystick module KY-023
1 xTouch Sensor ModuleKY-036
1 x Enclosure box
1 x Analog magnetic sensor module KY-035
1 x Mercury sensor + LED module KY-027
1 x Rotary encoder module KY-040
1 x Optocoupler module KY-010
1 x Pulse sensor KY-039
1 x Reed relay module KY-025
1 x Obstale sensor module KY-032
1 x Line following sensor module KY-033
1 x Microphone module KY-038
1 x Laser module KY-008
1 x 5V relay module KY-019
1 x Temperature module module (DS18B20) KY-001
1 x Temperature module module (LM35) KY-028
1 x Linear magnetic sensor module KY-024
1 x Fire sensor module KY-026
1 x Sensitive microphone module KY-037
1 xTemperature and humidity sensor module (DHT11) KY-015
1 x XY joystick module KY-023
1 xTouch Sensor ModuleKY-036
1 x Enclosure box

## Slide 9
  HAL 综合范围 HAL integrated scope
HAL 中集成了两个简单的信号显示器。
双击要显示的信号，打开一个显示窗口，可以更改刻度和时基。
信号，无论它是什么，都从 1 缩放到 1000。
Two simple signal displays are integrated into the HAL.
Double click on the signal to be displayed and a display window opens with the possibility of changing the scale and the time base.
The signal, whatever it is, is scaled from 1 to 1000.

## Slide 10
  插槽命名 Slot naming
如图所示，使用简单的测试文件将已识别的名称分配给插槽。
您可以选择设置最小值和最大值，以便以简化的方式增强显示的值。
Identified names are assigned to slots using a simple test file as shown.
You can optionally set minimum and maximum values so that the values shown can be enhanced in a simplified way.

## Slide 11
  自动化语言 The AUTOMATION LANGUAGE

## Slide 12
  自动化语言 The AUTOMATION LANGUAGE
编程语言 THEREMINO AUTOMATION 是在无数请求之后生成的，以便能够以简单的方式对插槽进行编程。
它是一种非常强大的语言，它包含其他程序所没有的功能。
它有一个报告编程错误的系统。
它允许您在运行时查看数据和变量。
一个非常简单有效的调试器。
对于那些不是专业程序员但具有编程基础的人来说，它拥有让生活更轻松所需的一切。
The programming language THEREMINO AUTOMATION was generated following the countless requests to be able to program the slots in a simple way.
It is a very powerful language, it contains functions that other programs do not have.
It has a system that reports programming errors.
It allows you to view data and variables at run time.
A very simple and effective debugger.
It has everything you need to make life easier for those who are not a professional programmer, but who have the basics of programming.

## Slide 13
  变量赋值 Variable assignment
变量的管理被简化。
除了声明变量之外，还声明了槽位和分配的编号
The management of variables is simplified.
In addition to declaring the variables, the slots and the assigned number are also declared

## Slide 14
  按钮 – 文本、插槽、颜色、标签、启用/禁用 Buttons – text, slot, color, labels, enable/disable
已生成用于管理按钮的简化结构，您可以为其分配文本、插槽、颜色以及启用和禁用它们
A simplified structure for the management of buttons has been generated, to which you can assign text, a slot, the color and enable and disable them

## Slide 15
  路由指令 Routing instructions
Gosub - Return
For- next, with step
If - Else - Endif
Select case

## Slide 16: Theremino devices
… and much more.
……还有许多其他人。

## Slide 17: For more info, search the word: “theremino”
THANKS FOR YOUR TIME
谢谢你的时间
欲了解更多信息，请搜索词：“theremino”